## Slide 1: CO2 Reduction Potential of Global Supply Chain Networks: An MRIO Approach Incorporating Maritime Network Structures
Tomomi SHODA1, Keitaro MAENO2, Taiga SHIMOTSUURA1, and Shigemi KAGAWA3
1 Graduate School of Economics, Kyushu University, Japan
2 National Institute of Advanced Industrial Science and Technology, Japan
3 Faculty of Economics, Kyushu University, Japan

## Slide 2: 1. Introduction
The Paris Agreement was adopted in 2015 to tackle climate change and its negative impacts, and more than 120 countries and regions have set a goal of “net zero carbon dioxide emissions” (United Nation, 2016).
The global supply chain (GSC) structure has significantly developed over the past few decades driven by the expansion of international trade.
23% of global CO2 emissions are embodied in traded goods through GSCs, and 30% of consumption-based emissions of wealthy countries were imported, indicating the potential for international carbon leakage (Davis et al., 2011).
Environmentally Extended Multi-Regional Input-Output (EE-MRIO) models are one of the most powerful tools for tracing GSCs and allocate emissions from production to consumption across countries (Vershuur et al., 2022 & Fry et al., 2024).
1/26

## Slide 3: 1. Introduction
In Input-Output Analysis, Multi-Regional Input-Output (MRIO) tables describe inter- and intra-industry dependencies within and between countries by modeling GSCs as a multidimensional space defined by country, commodity, and industry (Vershuur et al., 2022 & Fry et al., 2024).
However, MRIO tables do not provide insights into the domestic and international transportation systems used for these trade flows, as paths through physical space are not explicitly defined (Fry et al., 2024).
On the other hand, the development of the GSCs has led to the geographic separation of production areas and consumption areas (Wiedmann & Lenzen, 2018).
Therefore, current GSC is highly dependent on international shipping (UNCTAD, 2021).
2/26

## Slide 4: 1. Introduction
To more accurately evaluate the environmental impact of GSCs, it is essential to develop analytical EE-MRIO methods that incorporate physical dimensions.
To develop a new framework to analyze trade flows transported by international container shipping based on MRIO.
To estimate CO2 emissions from international container shipping induced by GSCs and allocate CO2 emissions to countries.
🇨🇳 ?%
🇯🇵 ?%
🇺🇸 ?%
🇩🇪 ?%
Objective
3/26

## Slide 5: 2. Methodology
Estimation of CO2 emissions from international container shipping using MRIO (Conceptual)
: Offshore CO2 emissions matrix for
international container shipping
: CO2 emission intensity matrix for
international container shipping
: Container transport ratio matrix
: Identity matrix
: Input coefficient matrix
: Diagonal matrix of global final demand
: Leontief inverse matrix
: CO2 emissions from international shipping induced by global final demand through GSCs
: direct and indirect input induced by global final demand
: direct and indirect input transported by container shipping induced by global final demand
4/26

## Slide 6: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
Adjacency matrix weighted by CO2 emissions (t-CO2) from container ships between 893 ports
Row element the departure port
Column element the arrival port
the total amount of CO2 emissions from container ships departing from 𝑖-th port and arriving at 𝑗-th port
5/26

## Slide 7: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
Flaw of the adjacency matrix is that only direct transport is recorded. e.g. Hamburg (Gremany) – Tokyo (Japan): 0 t-CO2
Estimation of CO2 emissions of each voyage (t-CO2)
Arrival time :
Departure time :
Carbon intensity: (t-CO2/h) Speed : (km/h)
Voyage time: (h)
CO2 emissions: (t-CO2)
6/26

## Slide 8: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
Reallocating CO2 emissions attributed to hub ports to origin ports
To overcome the flaw, shortest path is used for estimation of CO2 emissions from indirect transport based on graph theory and economics of scale.
Before
After
7/26

## Slide 9: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
Shortest path based on graph theory and economic of scale
Based on economies of scale, the more a certain route is used, the lower the cost becomes, which in turn leads to even greater usage of that route.
Based on shortest path, the most cost-effective route between any two ports is calculated.
port
cost to pass through
8/26

## Slide 10: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
CO2 emissions reallocation based on shortest path
e.g. Hamburg (Gremany) – Tokyo (Japan)
Hamburg – Rotterdam – Suez Canal – Singapore – Johor – Hong Kong – ZhouShan – Okpo – Yokohama – Tokyo
However, Suez Canal – Singapore does not only appear on Hamburg – Tokyo.
Suez Canal – Singapore appears also on Hamburg – Shanghai, Antwerp – Hong Kong, and so on …
CO2 emissions from Suez Canal – Singapore need to be reallcated to all paths where it appears.
9/26

## Slide 11: 2. Methodology
Estimation of CO2 emission intensity matrix for international container shipping – CO2 emission (Conceptual)
CO2 emissions reallocation based on shortest path
The rate of reallocation to all paths is based on trade value between countries where ports belong to.
893
ports
164
regions
10/26

## Slide 12: 3. Data
Multi-Regional Input-Output Database GLORIA 2019 (Lenzen et al., 2021)
International shipping database Sea-web Database (IHS Markit Ltd) voyage histories in 2019 of container ships owned by top 10 container shipping companies (84% of full containers in the world) Carbon intensity estimated in bottom-up method (IMO, 2021)
Trade statistics Trade Statistic Data for Japan – Sea Container Cargo Commodity by Country – Import (2019) (Ministry of Finance Japan, 2020)
Due to data limitation, this study takes Japan’s import as a case.
11/26

## Slide 13: 4. Results
Critical international shipping ports in terms of frequency of appearance in the 797,449 (893×893) shortest paths
12/26

## Slide 14: 4. Results
Singapore is the most critical port, highlighting its role as a global maritime hub port.
13/26

## Slide 15: 4. Results
Rotterdam is second most critical port, highlighting its role as a regional maritime hub port.
14/26

## Slide 16: 4. Results
Ports like Johor, Antwerp, Piraeus, and Busan reflect their importance as regional gateways that connect smaller ports to the global network.
15/26

## Slide 17: 4. Results
The presence of Panama Canal and Suez Canal highlights their geographic importance as vital corridors.
16/26

## Slide 18: 4. Results
The prominence of Asian ports emphasizes East Asia and Southeast Asia’s centrality in international container shipping and central role in GSCs.
17/26

## Slide 19: 4. Results
Japan’s import by container shipping induced by global final demand was 317.14 billion USD.
18/26

## Slide 20: 4. Results
CO2 emissions from international container shipping induced by Japan’s Import was 12.91 Mt-CO2.
19/26

## Slide 21: 4. Results
CO2 emission intensity of international container shipping toward Japan was 40.7 kg-CO2/1000 USD.
20/26

## Slide 22: 4. Results
Asian countries (e.g., China, South Korea, Vietnam, Thailand) generally show lower CO2 emission intensity of international container shipping.
21/26

## Slide 23: 4. Results
Distant countries (e.g., USA, Russia) show higher CO2 emission intensity, reflecting longer transport distances.
22/26

## Slide 24: 4. Results
India has the highest CO2 emission intensity, indicating inefficient or long-distance shipping routes.
23/26

## Slide 25: 4. Results
Despite the geographical distance, Germany shows relatively low CO2 emission intensity, reflecting efficient logistics and high-value exports.
24/26

## Slide 26: 5. Discussion
For GSC restructuring
According to Maeno et al. (2022), the restructuring of the GSC has the potential to significantly reduce the carbon footprint of production.
For governments, it is crucial to establish trade policies to facilitate the transition of import destinations under the context of decarbonization.
When CO2 emission intensity of production and CO2 emissions from procuction is similar, CO2 emission intensity of international container shipping estimated in this study is an index for deciding production countries.
More specific and inclusive policy implications for GSC restructuring are possible by combining model developed in this study with usual EE-MRIO model.
25/26

## Slide 27: 6. Conclusion
Singapore is the most critical port for GSCs, and East Asia and Southeast Asia are most critical areas for GSCs in terms of international container shipping.
Asian countries show lower CO2 emission intensity of international container shipping to Japan, while Distant countries show higher CO2 emission intensity, reflecting longer transport distances.
Geographical distance does not necessarily lead to higher CO2 emission intensity of international container shipping.
When CO2 emission intensity of production and CO2 emissions from procuction is similar, CO2 emission intensity of international container shipping estimated in this study is an index for deciding production countries.
26/26

## Slide 28: Thanks for your attention! Tomomi SHODA Kyushu University Email: shoda.tomomi@gmail.com