## Slide 1: Life-cycle CO2 circulation of direct air capture and methanation: an input-output analysis
Mitsuo Yamada (Chukyo University)
Keiko Nakayama (Chukyo University)
Soichiro Masuda (Toho Gas, Co., Ltd.)
Koyo Norinaga (Nagoya University)
The 32nd International Input-Output Association Conference/IIOA2026
Spain/Seville, June 23-16, 2026

## Slide 2: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 3: Introduction
Direct air capture (DAC) is a useful step toward achieving carbon neutrality.
  There are several variations of the method.
Cryo-DAC ( currently being developed by Nagoya University and Toho Gas ) absorbs CO2 from the atmosphere using a CO2 absorption liquid, and in the regeneration process, unused cold energy from liquid natural gas (LNG) is used.
  Using the unused cold energy, instead of fossil fuels, is advantageous for effectively reducing CO2 emissions.
Our Research Questions
How much is CO2 emitted by Cryo-DAC?
Whether is it able to capture more CO2 than is emitted?
How much is the LC-CO2 of the CO2 circulation system of Cryo-DAC and methanation?
Cryo-DAC is being developed as part of the NEDO Moonshot Research and Development Program, Goal 4: Realizing sustainable resource circulation to recover the global environment by 2050, under the project "Research and development toward saving energy for direct air capture with available cold energy," run by Professor Norinaga of Nagoya University as project manager. In addition to Nagoya University and Toho Gas, Chukyo University, Tokyo University of Science, the University of Tokyo, and private companies such as JGC, and AGC also participate in this research.

## Slide 4: In this study, we apply hybrid method of mainly input-output method and partly process-based method
Method | Domestic goods | Imported goods
Input-output method | ・Input-output table, Japan (2020 Table, 390 sectors) ・3EID (Embodied Energy and Emission Intensity Data for Japan Using Input－Output Tables) database 2020 edition, by the National Institute for Environmental Studies (NIES). | 2020 table of ・OECD Inter-Country Input-Output (ICIO) tables, 2025 edition ・Greenhouse gas footprint indicators, 2023 edition
Process-based method | - | Only for Coal, oil, natural gas, and hydrogen, ・AIST-IDEA database, Japan
The monetary-base emission coefficients need to consider price changes between the base year and the concerned year. We consider changes in the input coefficients and direct CO2 emission coefficients of the electricity and steel sectors, which have high CO2 emissions, under a CO2 reduction scenario, as well as future effects on the CO2 emissions of our circulation system. |  | 

## Slide 5: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 6
The Cryo-DAC is a technology that directly captures CO2 from the atmosphere using unused LNG cold energy.
Figure 1 shows a conceptual.
  The absorption tower channels air through a CO2 absorption liquid that absorbs atmospheric CO2; after absorption, the air without CO2 is released.
  The liquid with absorbed CO2 is sent from the absorption tower to the regeneration tower, where CO2 is captured by a pressure swing.
  The captured CO2 is then sent to the sublimation tank, where it is solidified into dry ice using the cold energy supplied by LNG.
  As the dry ice solidifies, the pressure is reduced, thus accelerating CO2 regeneration in the regeneration tower. (Pressure-Swing regeneration)
  In addition, dry ice can be recovered as liquid or gas.
Cryo-DAC does not require external energy input to restore CO2 from the absorption layer, which reduces the energy costs and lowers overall CO2 emissions.
Source: Slide-5 of Norinaga (2023)
Figure 1 Conceptual diagram on Direct capture of atmospheric CO2 by Cryo-DAC
Currently, we are developing a system with the capacity to capture 200,000 tons-CO2 per year, with the aim of reducing costs. This cost is expected to become comparable to the DAC of leading overseas companies in the future.
Cold energy solidifies the captured CO2 into dry ice, which reduces the pressure, thus accelerates CO2 regeneration (Pressure-Swing regeneration)

## Slide 7
CO2 in the atmosphere
【Cryo-DAC】
CO2
captured
【Methanation】
CH4
4H2
2O2
2H2O
2H2O
【Renewable energy power】
【Desalination】
【Water
electrolysis】
CO2
Energy
CO2
Energy
CO2
Energy
CO2
Energy
CO2
Energy
CO2 circulation system
of Cryo-DAC and Methanation
Hydrogen supply
LNG Cold Energy
CO2: -100
CO2: +100

## Slide 8
Source: Created by the authors.
Figure 2 System boundaries of the CO2 circulation with Cryo-DAC and methanation
【System boundaries of the CO2 circulation model using the Cryo-DAC and methanation】
LNG that supply cold energy does not included in the CO2 circulation system, as the cold energy is surplus and .
(Ⅰ) Subsystem boundary of Cryo-DAC only
whether the Cryo-DAC system alone captures more CO2 than that emitted during the production of the energy and resources required to capture CO2 from the atmosphere
if so, the extent to which the system offsets CO2 emissions by capture.
(II) Subsystem boundary of the CO2 circulation system with Cryo-DAC and methanation, excluding methane-consumption
In the CO2 circulation system, methane-consumption is excluded. Therefore, the LC-CO2 of the synthetic methane is targeting.
(Ⅲ) System boundary of Cryo-DAC and methanation CO2 circulation system, including methane-consumption
whether the amount of CO2 emitted by this system is sufficiently small remains?

## Slide 9: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 10: Input output model
Basic model
Induced production
CO2 emissions
Embodied CO2 emission coefficients
Case 1

## Slide 11
Model including imported goods
Induced production in the foreign country stemmed from the import demand of home country.

## Slide 12
LC-CO2 emission in the model including imported goods
Case 3
Case 2

## Slide 13
LC-CO2 emission in the international model
Case 4

## Slide 14
Case No. | Equation | Eq. No. | Assumptions
Case 1 |  | (7) | ・No imports or imported goods are produced in home country. ・Domestic and imported goods are produced using the same technology. ・The induced effect from the production of imported goods to the domestic production is considered.
Case 2 |  | (26), (18), (20) | ・Imported goods are produced in foreign countries. ・Domestic and imported goods are produced using the same technology. ・There is no induced effect from the production in foreign countries to home.
Case 3 |  | (24), (18), (20) | ・Imported goods are produced in foreign countries. ・Different technology is used for producing domestic and imported goods. ・There is no induced effect from the production in foreign countries to home.
Case 4 |  | (29) | ・Imported goods are produced in foreign countries. ・Different technologies are used in producing domestic and imported goods. ・The induced effect from the production in foreign countries to home is considered.
Foreign country
Home country
F
X
c
B
E*
X*
c*
B*
*
F
Xd
cd
Bd
Md
AmBd
c
Case 1
Case 3
Case 4
Case 2
Bd
Independent demand
Leontief inverse
Induced production
Emission coefficient
CO2 emission
Table 2 Variation of the embodied CO2 emission coefficients
Complete model
Detailed model

## Slide 15
By, using OECD-ICIO database, Yamada, and et.al. (2026) shows that the assumption of same technologies and CO2 emission factors between home and foreign countries induces lower estimates of LC-CO2 emissions.
If the sector size of foreign country is same as home, the Case 3 is better choice than Case 1-2 to evaluate the LC-CO2 emissions.

## Slide 16
LC-CO2 calculation of the CO2 circulation system
Exogenization
Induced production
CO2 emissions, except the 3rd sector

## Slide 17: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 18
CO2 in the atmosphere
【Cryo-DAC】
CO2
captured
【Methanation】
CH4
4H2
2O2
2H2O
2H2O
【Renewable energy power】
【Desalination】
【Water
electrolysis】
LNG: 250
CO2: 200
CO2 circulation system
of Cryo-DAC and methanation
Capacity of Cryo-DAC:
200 thousand ton/year
Estimate capital goods and inputs of each process
Hydrogen supply
LNG Cold Energy
CO2: -200
CO2: 200
H2: 36.4
H2O: 327.3
CH4: 72.7
Unit: thousand ton

## Slide 19
Table 3 Production and main materials in the CO2 circulation system
【the production and main raw materials in each process of the CO2 circulation system】
Case 1 shows the relationship when 1 ton of LNG that supplies cold energy to the Cryo-DAC.
Case 2 shows that a Cryo-DAC facility operates to capture 200,000 tons of CO2 per year.
Process | Performance and costs | Reference
LNG | CO2 emissions from LNG refining, liquefaction, transportation, and other processes were estimated | Pospíšil et. al. (2019), and NEDO (2018)
Cryo-DAC | OPEX/CAPEX obtained from the simulation using the AspenPlus | From our research
Synthetic methane | 12.5 Nm3/h, 100-200 million yen | IHI (2022) Press release 2022/10/21
Hydrogen production | 300 (Nm3/h)/unit, 78 million yen/unit | The Institute of Applied Energy (2020)
Renewable energy generation | Operation rate 20%, daily power generation 2.7 kWh/kW, and 288 thousand yen/kW, 38% cost reduction | Website of TEPCO Energy Partner inc. (2024)
Desalinated water | 500 t/day, 630 thousand yen /(m3/day), 60% cost reduction | Website of Ace Water Treatment Co., Ltd.
We estimated the intermediate inputs, added value, and capital investment amounts of the input-output model
The capital costs were estimated based on the performance and cost of the equipment as assumed from various source listed in Table 3.
Some cost reduction was assumed in power generation and water supply because of scale efficiency.
Capital investment was calculated as the annual average amount divided by useful life.
Table 4. Sources for CO2 circulation system cost estimates

## Slide 20
Source: Computed and Drawn by the authors.
Figure 3 Cost structure of the CO2 circulation system with Cryo-DAC and methane production
Figure 3 shows the cost breakdown for the CO2 circulation system.
Here, capital goods are expressed as the annual investment amount (fixed capital depreciation), calculated by dividing the equipment investment amount by its useful life.
For CO2 capture, the cost of LNG used to supply cold energy was excluded.
In the cost structure of Cryo-DAC, capital goods accounted for the largest amount at 38.8%, followed by others at 26.3%, absorption liquids at 18.6%, and electricity at 9.0%. Other costs included maintenance costs.
For hydrogen production, 75.5% of hydrogen production is electricity cost. Here, all renewable energy generation costs that supply electricity for hydrogen production were included in the electricity costs. Water desalination costs are also included in the others.
For the synthetic methane, hydrogen production accounted for the largest proportion at 51.1%, followed by CO2 capture costs at 27.1%.
Although capital costs are more important than absorption liquid and electricity for the cost structure of the Cryo-DAC alone, electricity is the most important factor in the costs of the total system.

## Slide 21
Figure 4 Procedure for determining the embedded CO2 emission coefficients
Domestic
Goods
Imported
Goods
Import taxes
AIST: National Institute of Advanced Industrial Science and Technology

## Slide 22
Preprocessing before estimating the LC-CO2 emissions through input-output analysis with 3EID(NIES).
the conversion from the purchaser price-based estimates to producer price-based by using the trade and transport margin rates from the 2020 Input-Output Table (390 sectors).
the conversion to the 2020 price evaluation to obtain the LC-CO2 by the CO2 emission coefficients of monetary units-base.
We obtain the price index by sector from 2020 to 2023, corresponding to the input-output model from the Corporate Price Index (Bank of Japan), Consumer Price Index (Ministry of Internal Affairs and Communications), Agricultural Price Statistics (Ministry of Agriculture, Forestry, and Fisheries), and Employee Income per capita (Cabinet Office).
For the sector, the price data of which are not available, is estimated as the average of the obtained sector’s price indices and employee income per capita index with weights of input coefficients.
Monetary-base CO2 emission coefficients:
volume-based CO2 emission:
This does not differ from calculating the amount of CO2 emissions based on the amount of CO2 emissions by material volume.
If p1>p0, then CO2*>CO20, and if p1<p2, then CO2*<CO20, correlating to an amount that is either too high or too low.
In such cases, if the expenditure revalued at the base year prices, a value equivalent to the CO2 emissions is evaluated in physical terms, as shown below.

## Slide 23
Price adjustment due to difference in the quality
The prices of individual materials in the system may deviate from the average prices of the corresponding sector. This also overestimates or underestimates CO2 emissions in the input-output analysis.
As an example of quality adjustment, the price of some materials, such as stainless steel, set in the Aspen Plus simulation was higher than the average price of the corresponding sector.
In addition, the electricity price is assumed to be lower than the average price in the electricity sector.
Using an open model in the input-output analysis, the induced production and imports are calculated for exogenous demand
See I-O model/Case 3 and Figure 4
where p1q is the price of a material that differs in quality from the average goods in the corresponding sector.

## Slide 24: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 25: Results
We calculated
the domestic production spillover effect of intermediate goods due to exogenous production
and the production spillover effect (here called the import spillover effect) when the induced import demand is produced domestically.
In addition to the spillover effect of intermediate goods, we calculated the domestic production and import spillover effects due to the annual capital investment amount corresponding to the depreciation of fixed capital.
These effects are expressed as relative values, with the exogenous production value of the CO2 circulation system set to 1.
Table 4 Exogenous production and corresponding production and import spillover effects
The amount of production induced in the base year, together with the exogenous production, was 1.948 times the production amount.

## Slide 26
Table 5 LC-CO2 of the CO2 circulation system with Cryo-DAC and methanation Unit: t-CO2
Source calculated by the authors.
【 LC-CO2 of the CO2 circulation system with the Cryo-DAC, methanation, and LNG as cold energy sources 】
We estimated the CO2 emissions and capture amounts as well as the net CO2 emissions for each processes; Cryo-DAC, hydrogen production, synthetic methane production, and integrated CO2 circulation system, both with and without LNG.
【 Estimations for three periods: 2020, 2030, and 2040 】
The present period is 2020, which is the base year for the input-output table.
For 2030 and 2040, we assumed various CO2 reduction measures that will occur in the electricity and steel sectors.
  Electricity and steel sectors are the major sources of CO2 emissions and are closely related to the Cryo-DAC and methanation CO2 circulation system.
  The impacts of their decarbonization that would occur are examined.
Note Cryo-DAC: Effective CO2 capture rate (%) = Net CO2 Captured / CO2 Captured × 100 CO2 circulation system: CO2 reduction rate (%) = Net CO2 emissions / CO2 captured ×100 CO2 circulation system with methane consumption: CO2 reduction rate (%) = (1- Net CO2 emissions / CO2 captured) ×100

## Slide 27
Source Calculated and drawn by the authors.
Figure 5 LC-CO2 impacts of the Cryo-DAC, excluding cold energy supply
【 LC-CO2 emissions for Cryo-DAC】
Presently, 87.5 thousand tons of CO2 are emitted to capture 200 thousand tons of CO2. As net, 112.50 thousand tons were captured. This was the effective capture amount, with a ratio of 56.25%.
  Electricity accounted for the largest proportion of CO2 emissions at 85,700 tons of emitted CO2.
  The CO2 emissions from fuel, absorption fluid, maintenance, and capital goods production are smaller than those from electricity.
Future changes in the power supply mix and the decarbonization of the steel industry
  CO2 emissions from electricity will decrease significantly to 49.49 thousand tons in 2030 and 15.2 thousand tons in 2040.
  The effective CO2 captured amount will increase to 132.06 thousand tons in 2030 and 170.41 thousand tons in 2040: the effective capture rates are 66.03% and 85.21%, respectively.
Cryo-DAC could capture more CO2 than it emits.
At present, the effective capture rate is below 50%, as the use of grid power.
The future change in the power supply mix and decarbonization of the steel industry decrease the CO2 emission, and effective capture rates will increase.
Negative net LC-CO2 emissions
of Cryo-DAC
Effective capture rates
56.25% 66.03% 85.21%

## Slide 28
Source Calculated and drawn by the authors.
Figure 6. LC-CO2 effects of the CO2 circulation system, excluding cold energy supply and methane-consumption
【 LC-CO2 emissions from the CO2 circulation system, excluding cold energy supply and methane-consumption 】
CO2 emission of 200 thousand tons, which are emitted at the consumption stage of methane, are not included.
The current CO2 emissions are 162.54 thousand tons during the production process; 84.79 for electricity, 47.56 for capital goods, 25.67 for maintenance and others.
As 200 thousand tons of CO2 is captured from the atmosphere by Cryo-DAC, the net CO2 emissions of this system is -37.46 thousand tons. The reduction rate is 18.73% .
This CO2 reduction effect is considered as a new environmental value of synthetic methane in our CO2 circulation system.
Due to future changes in the power source mix and decarbonization of the steel sector, this reduction rate is expected to increase to 35.94% by 2030 and 65.99% by 2040.
Negative net LC-CO2 emissions
of synthetic methane
Energy inputs to maintain the circulation
CO2 captured by Cryo-DAC
Effective reduction rates
18.73% 35.94% 65.99%

## Slide 29
Source Calculated and drawn by the authors.
Figure 7 LC-CO2 emissions of the CO2 circulation system with Cryo-DAC and methanation, excluding cold energy supply but including methane-consumption
【 LC-CO2 emissions from the CO2 circulation system, excluding cold energy supply and including methane-consumption. 】
CO2 neutral part of the synthetic methane
  200 CO2 are captured, and 200 CO2 are emitted when consumed.
  By recycling CO2, it is possible to reduce CO2 emissions to zero.
Maintaining part of the circulation system
  In 2020, the LC-emissions associated with the system amount to 162.54 thousand tons,
  Net CO2 reduction of 37.46 thousand tons through this circulation system. This is 18.73% of the CO2 circulation volume.
The decarbonization in electricity and iron and steel sectors reduces the CO2 emissions; 128.12 for 2030, and 68.01 for 2040.
These increase CO2 reduction volume 71.88 for 2030, 131.99 for 2040, which are relatively 35.94% and 65.99% of the CO2 circulation for each year; same values in Figure 6.
Methane consumption
CO2 captured by Cryo-DAC
Energy inputs to maintain the circulation
Effective reduction rates
18.73% 35.94% 65.99%
Effective reduction of CO2 circulation

## Slide 30
Source: Calculated and drawn by the authors.
Figure 8. LNG substitution effect by synthetic methane in the CO2 circulation system
Substitute LNG
Since synthetic methane is the primary component of LNG, we can assume that the synthetic methane substitutes LNG, provided the overall demand for LNG remains constant.
200.0 thousand tons of CO2 circulating within the material cycle maintain carbon neutrality.
The system does, however, incur 162.54 thousand tons of indirect life-cycle emissions for its maintenance, which represent positive net emissions.
Conversely, the substitution of LNG avoids a total of 256.79 thousand tons of CO2 emissions; 200.0 from consumption, 49.67 from imports, and 7.11 from intermediate goods.
The 162.54 thousand tons of net emissions in the circulation system and 256.79 thousand tons through LNG substitution, resulting in a net CO2 reduction of 94.25 thousand tons. This volume is evaluated as 47.12% of the circulated CO2 volume, 200 thousand tons.
Owing to future changes in the power source mix and decarbonization of the steel sector, the CO2 reduction rate will increase to 63.47% in 2030 and 91.73% in 2040.
【 LNG substitution effect 】
Methane consumption
CO2 captured by Cryo-DAC
Energy inputs to maintain the circulation
LNG production and transport
+162.54 -256.79
CO2 emission
-94.25 -126.94 -183.46
Net CO2 emission
LNG substituted

## Slide 31: Contents
Introduction
Background
Input-output model
Assumption of the CO2 circulation system and database
Results
Conclusions
Appendix A: Future changes in the input and CO2 emission coefficients in the electricity, and iron-steel sectors
Appendix B: Multi-country input-output database

## Slide 32: Conclusions
We assumed a CO2 circulation system in which synthetic methane is produced from CO2 captured by a Cryo-DAC and green hydrogen, used it as a raw material for city gas, and estimated the LC-CO2 mainly using an input-output model.
Considering Cryo-DAC alone, the amount of CO2 captured by the DAC was greater than the amount emitted, making this an effective method.
Of the 200 thousand tons of CO2 captured, 112.5 (56.25%) are effectively captured.
If currently grid electricity is used, CO2 emissions will remain high.
Owing to changes in the power source mix in the future and decarbonization of the steel sector, CO2 emissions are expected to decrease, the effective CO2 capture rate of Cryo-DAC is to increase to 66.03% in 2030 and 85.21% in 2040.
Improve the efficiency of power usage and expansion of carbon-free and/or renewable energy electricity are expected furthermore.
LC-CO2 emissions in the CO2 circulation system of the Cryo-DAC and methane production, excluding cold energy supply. Positive CO2 emissions to maintain circulation exist but will decline due to decarbonization of power and steel industries.
The 200 thousand tons of captured CO2 becomes synthetic methane, which is consumed and released into the atmosphere, creating CO2 circulation. It shows CO2 neutral, but CO2 is emitted when energy and resources are input to maintain the circulation system.
Currently, 162.54 thousand tons are emitted. Therefore, although 200,000 tons of CO2 emissions were captured, only 37.46 thousand tons of CO2 are effectively reduced. This is equivalent to 18.73%, which was lower than expected.
Due to future changes in the power source-mix and decarbonization of the steel sector, this proportion is expected to increase to 35.94% in 2030 and 65.99% in 2040, gradually approaching a CO2 neutral state.

## Slide 33
Furthermore, considering LNG substitution effect by the synthetic methane in our CO2 circulation system, negative reduction of CO2 emissions is expected.
Currently, the combustion of synthetic methane returns 200.0 thousand tons of captured CO2 to the atmosphere, while its production incurs 162.54 thousand tons of indirect life-cycle emissions.
However, assuming this synthetic methane substitutes an equivalent volume of LNG, the overall system achieves a net CO2 reduction of 94.25 thousand tons.
Thus, the LNG substitution reduces CO2 emissions, which is 47.12% reduction rate compared with the CO2 circulation volume of 200 thousand tons.
This rate is expected to increase to 63.47% in 2030 and 91.73% in 2040 due to changes in the power source structure and decarbonization of the steel sector.
The introduction of a CO2 circulation system using a Cryo-DAC and synthetic methane could potentially bring us closer to a carbon-neutral state if the electricity used is decarbonized.
To introduce such a CO2 circulation system on a scale, the production cost of synthetic methane must be reduced to a level that is sufficiently competitive with competing energy prices, such as LNG.
To achieve this, the cost of Cryo-DAC ought to be reduced, inexpensive hydrogen must be made available, and methanation costs must decrease. These costs should be investigated in depth in future research.