## Slide 1: Assessing the environmental impact of CE policies
A case study of Electric and Electronic Equipment in Flanders
IIOA Conference 2026
Dani Sangers & Pieter Fonteyn

## Slide 2: Agenda
Methodology
Material Flow Analysis
Dynamic Stock-Flow Model (SF)
Scenario modelling
Extending EEMRIO with Flanders
Creating prospective tables
Linking SF to EEMRIO

## Slide 3: Methodology
Material Flow Analysis
1.
2.
3.
Dynamic Stock-Flow Model
Policy scenarios
Extended EEMRIO model
4.
Environmental impact assessment
5.
Case study: Electronic and Electrical Equipment (EEE) in Flanders

## Slide 4: Methodology
Material Flow Analysis
1.
2.
3.
Dynamic Stock-Flow Model
Policy scenarios
Extended EEMRIO model
4.
Environmental impact assessment
5.
Case study: Electronic and Electrical Equipment (EEE) in Flanders
Map current EEE flows and identify key stocks and flows.
Model future material stocks and flows until 2050.
Model CE policy interventions through what-if scenarios.
Extend the FIGARO-e3 input-output model with the Flemish region.
Translate the material flow changes into monetary effects and estimate the carbon footprint of EEE consumption.

## Slide 5: Material Flow Analysis

## Slide 6: Material Flow Analysis
Mapped EEE system from put on market to end-of-life
Captured key stocks and flows
  In-use stock, repair, reuse, waste collection, recycling, energy recovery and disposal
Integrated multiple data sources to quantify flows and identify data gaps:
  WEEE Calculation Tool (POM, lifetimes, waste generation)
  Eurostat (EU-6 waste management statistics)
  Recupel
  BeWeee
  PV Cycle Belgium
Identified possible CE intervention points
Creating a conceptual material flow diagram

## Slide 7: Mapping material flows

## Slide 8: Dynamic stock-flow model

## Slide 9: Development of stock model
Based on WEEE Calculation Tool Belgium
  At UNU Key level (54 product categories)
  Historic POM data (1980-2022)
  Weibull parameters
  Result: estimate of waste generated
  Expanded to include stock estimate, modeling in units and tonnes (based on avg unit weights)
Derive household stock, create projections (logistic trend) for 2023-2050
  Multiply by estimates of number of households in Flanders  projected total stock Flanders
Dynamic stock model: recursively estimate POM quantities
  Based on projected stock evolution, estimate of waste generated, and estimate of reused products

## Slide 11: Policy scenarios

## Slide 12: Policy scenarios
Put on market phase: enabling circularity from the outset
  Ecodesign and durability requirement, repairability and upgradability requirements, …
Use phase: extending and intensifying product lifetimes
  Repair and maintenance incentives, support for local repair ecosystems, …
Post-use phase: preparing products for further use
  Reuse targets, quality standards, public procurement for refurbished, …
End-of-life phase: closing material loops and managing residual waste
  High-quality recycling requirements, improved collection systems, …
Reduce dormant products
Extended active use
Improved collection
Increase reuse
Increased lifetime during reuse
Refuse
Combined scenario 1-5
Combined scenario 1-6
Possible circular policy interventions
8 policy scenarios

## Slide 13: Results stock-flow model
Baseline, 2015 vs. 2050, in tonnes
Intervention results, 2050, in tonnes
Intervention | 2030 | 2050
1. Reduce inactive life (selected products only) | -5% | -15%
2. Extend active life | +5% | +15%
3. Improve collection | +5% | +15%
4. Increase reuse | +5% | +15%
5. Extend reuse life | +5% | +15%
6. Reduce consumption | No change | -3%

## Slide 14: Extending the EEMRIO model with the Flemish region

## Slide 15: Extending FIGARO-e3 with the Flemish region
FIGARO-e3
Global multiregional input-output model: 45 regions + rest-of-world, 213 products, 176 industries
Built from inter-country supply & use tables (CPA 2.1 / NACE 2.1)
Extended with GHG emissions (CO₂, CH₄, N₂O, F-gases) and an EXIOBASE-based material footprint
Flemish IO Model
Based on 2015 Belgian interregional supply & use tables: 145 industries, 147 products
Multi-regional: Flanders, Wallonia, Brussels-Capital, extra-regional
Same environmental extensions as FIGAROe3: climate change impact (kg CO₂-eq) and material footprint
Extending FIGAROe3
Belgian region in FIGARO-e3 split into Flanders + rest-of-Belgium
Flemish classifications (SUT 2008 / SUTTAK-2008) converted to FIGAROe3's CPA 2.1 / NACE 2.1
Disaggregation uses Belgium's shares in FIGARO-e3 as allocation weights (incl. Flemish trade flows)

## Slide 16: Extending FIGARO-e3 with the Flemish region
Schematic overview of the extended FIGAROe3 use table integrating the Flemish use table

## Slide 17: Creating prospective SUTs

## Slide 18: Creating prospective SUTs: Two pathways to 2050
Projecting the Flemish-FIGARO-e3 tables to compare CE policies against two future baselines
Projected to 2050
Extended Flemish-FIGAROe3 SUTs, using GDP/population projections from the EC's Global Energy and Climate Outlook 2025
Pathway 1: Business-as-usual
Market forces + currently legislated climate policy
Exogenous GDP & population growth
Pathway 2: NDC-LTS
Builds on Pathway 1, adding 2030/2035 NDC targets
Plus long-term net-zero strategies beyond the NDC year
Both pathways serve as separate baselines: CE policy interventions are tested against each, comparing effectiveness under business-as-usual vs. a climate-ambitious future

## Slide 19: Linking SF to EEMRIO

## Slide 20: Translating CE Scenarios into the Prospective SUTs
Material flow changes from the scenario analysis were translated into three types of adjustments to the use table:
1. Recycled materials: intermediate use (matrix Z)
Additional recycled ferrous/non-ferrous metals, plastics and other materials substitute primary inputs in the largest-using Flemish industries; converted to monetary values using Eurostat waste collection & treatment prices (CPA 381/382).
2. Put on market: final demand (matrix Y)
Reductions in EEE products put on market are modelled as a one-on-one decrease in Flemish household final demand, after mapping UNU product codes to CPA 2.1; valued using Eurostat Belgian import data.
3. In-use stock: repair & maintenance demand (matrix Y)
Percentage change in physical EEE stock vs. baseline is applied to Flemish household demand for repair & maintenance services (SUT code 95A); not applied for Scenario 1 (dormant products) or Scenario 3 (collection).
The adjusted SUTs are then rebalanced (model D, Eurostat 2019), new input coefficients and Leontief inverses are derived, and combined with the environmental extensions to estimate the carbon and material footprint for each scenario.

## Slide 21: Results

## Slide 22: Results: Overall
Baseline vs. combined policy interventions, by pathway
Chart: Carbon footprint (kt CO2-eq)
| NDC-LTS — Combined | NDC-LTS — Baseline | BAU — Combined | BAU — Baseline
EU27 | 428 | 437 | 437 | 447
RoW | 3556 | 3629 | 4350 | 4457
Chart: Material footprint (kt)
| NDC-LTS — Combined | NDC-LTS — Baseline | BAU — Combined | BAU — Baseline
EU27 | 1858 | 1904 | 1914 | 1963
RoW | 10774 | 11265 | 11260 | 11790

## Slide 23: Results: Carbon footprint
Carbon footprint reduction of CE interventions in the Flemish EEE sector, occurring globally, compared to the baseline scenario (in kt CO₂-eq.).
Chart: 
| 1. Reduce dormant products | 2. Extended active use | 3. Improved collection | 4. Increase reuse | 5. Increase lifetime during reuse | 6. Refuse | 7. Combined scenario 1-5 | 8. Combined scenario 1-6
BAU | 3.3218 | -74.9547 | -1.9601 | -1.96 | -0.25629 | -42.5265 | -76.3654 | -116.4785
NDC-LTS | 2.4851 | -53.4192 | -1.4008 | -1.4008 | -0.16878 | -30.3128 | -54.3112 | -82.9058

## Slide 24: Results: Material footprint
Material footprint reduction of CE interventions in the Flemish EEE sector, occurring globally, compared to the baseline scenario (in kt).
Chart: 
| 1. Reduce dormant products | 2. Extended active use | 3. Improved collection | 4. Increase reuse | 5. Increase lifetime during reuse | 6. Refuse | 7. Combined scenario 1-5 | 8. Combined scenario 1-6
BAU | 14.4517 | -371.5842 | -9.6516 | -9.6513 | -1.5059 | -210.7782 | -380.5191 | -579.305
NDC-LTS | 13.2869 | -344.6551 | -8.9097 | -8.9093 | -1.4248 | -195.1606 | -352.9893 | -537.0284

## Slide 25: Discussion & conclusion

## Slide 26: Discussion
Upstream interventions (extending lifetimes, reducing demand)
  Largest carbon & material footprint reductions, in both pathways
Downstream interventions (collection, reuse)
  Limited benefits; most EEE impact sits upstream
  85% of avoided emissions/material use occur outside the EU27  Flanders' import-dependence
CE policy still delivers ~75% of its climate benefit even under a decarbonised (NDC-LTS) future
  CE and climate policy are complementary

## Slide 27: Conclusion & limitations
Conclusion
Stock-flow + EEMRIO modelling enables consumption-based, globally-traced CE policy assessment
Largest benefits = reduce/rethink/repair/reuse interventions, realised mostly outside Flanders/EU27
Limitations
Consumption-based view = partial picture; pair with economic, social, and territorial analysis
Aggregated EEMRIO structure limits product-level detail; recycling/repair sectors poorly captured
Static model: no technological change, price dynamics, or rebound effects

## Slide 28: Future research
More EEMRIO detail for R-strategy-relevant sectors
Add economic & social indicators
Explore a dynamic EEMRIO framework

## Slide 29: Appendix

## Slide 30: Dynamic stock-flow model
Purpose
  Projecting the evolution of EEE stocks and flows up to 2050
Conceptual approach
  POM → In-use stock → Waste generated (WG)
    Timing is determined by product lifetime distributions
  Links market dynamics, consumer stock, waste generation and treatment
  Allows the calculation of historic trends and future projections
Data sources
  WEEE Calculation tool (POM, Weibull parameters & waste generated)
  Federal Planning Bureau of Belgium (Population and household forecasts)
  Recupel (Downstream waste treatment and material composition)
Approach

## Slide 31: Dynamic stock-flow model
Main elements of the dynamic system
  Inflows: new products placed on the market (POM) and second-hand products re-entering the in-use stock through direct reuse (POM_RU) after waste collection.
  Stock: the in-use stock of EEE in households and businesses.
  Outflows: waste generated (WG), which is subsequently collected, reused, or treated.
  Treatment pathways: direct reuse, material recycling, other material recovery, energy recovery, incineration, and landfill
Estimation of the volume of EEE products put on market
  Based on stock changes, waste generation and direct reuse flows.
  Direct reuse and waste collection rates are calibrated using Recupel and Eurostat data
Modelling & lifetime assumptions

## Slide 32: Stakeholder workshop
Representation by OVAM, Recupel, PV Cycle Belgium, BeWeee, Agoria, Adevinta, Repair & Share, Herwin, Nelectra
Validate baseline assumptions for exogenous parameters in stock model
  Household stock projections*
  Expected service life (new* & reused products**)
  % waste collected***
  % direct reuse***
  % recycled***
Try to quantify impact of CE policy measures for EEE
  Proved difficult
  Modelled potential changes to exogenous parameters if CE policy measures would be successfully implemented
* Derived from WEEE Calculation Tool data
** Assumption 25% of new products
*** Based on Recupel, PV Cycle, BeWeee data